## Slide 1: Internship 2022 Progress report on E-tricycle Name: Njenga Emmanuel

## Slide 2: Tasks completed last week
[#20]Design of shaft
At 600rpm for the 1200W =19.10Nm
Using the maximum shear stress theory (Guest’s theory)
=
Diameter= 15.62mm

## Slide 3
[#21]Chain drive design
Design for the sprockets
Speed ratio=3.5
The larger sprocket=47T
Smaller sprocket = 15T
Design for the chain
D=180mm
d=70mm
Center distance ,x = 170mm
Chain length=
L=760mm

## Slide 4: Tasks in this week
[#31]Fabrication and assembly of the tricycle
[#32]Acquistion of parts
[#33]Calculation of power requirements for the shujaa tractor

## Slide 5: Timeline